## Slide 1: Catapult SystemC Matchlib Training July 2020
Stuart Swan
HLS IP/Platform Architect
July 2020
Source: Notes are in Tahoma, regular, 8 point, italic, flush left, vertically aligned from the bottom of text box.

## Slide 2: Basic SystemC and Matchlib Training
Stuart Swan
HLS IP/Platform Architect
July 2020
Source: Notes are in Tahoma, regular, 8 point, italic, flush left, vertically aligned from the bottom of text box.

## Slide 3: Why use SystemC + Matchlib for HLS?
SystemC provides HDL semantics on top of C++ language
  time, module structure, hierarchy, channels, HW semantics, resets, signals
SC enables time based behaviors to be cleanly modeled and verified prior to synthesis (as compared to pure C++ HLS)
SC integrates nicely with HDL simulators
Matchlib enables models to be “throughput accurate” pre-HLS
Matchlib provides commonly used components ready for HLS

## Slide 4: How does Catapult SC synthesis differ from C++ synthesis ?
Primary difference is in input language
Once code is read in by Catapult, 90% of flow and usage is same.

## Slide 5: Important to understand how HLS sees your SystemC model:
Set of processes communicating only thru signals (sc_signal<>)
For synthesis purposes, hierarchy is irrelevant (it is preserved in the RTL however)
HLS synthesis occurs on each process one at a time, in complete isolation
  No analysis/optimizations across processes
  Huge designs can be synthesized thru HLS, as long as each process is not too large
Each combinational process (SC_METHOD) becomes combinational logic in RTL
Each sequential process becomes exactly one FSM + Datapath in RTL

## Slide 6: How HLS sees your SC model (continued)
Primary optimizations done by HLS are in construction of the FSM and Datapath (e.g. resource sharing).
Unlike RTL synthesis, HLS is (usually) allowed to add clock cycles (latency) into design to improve QOR
  e.g. often loops are pipelined to maintain thruput while latency is added by HLS
Properly constructed models and proper usage of HLS should show no functional differences (aside from latency differences) pre and post HLS.
For SC HLS, reset behaviors and IO protocols are present in pre-HLS model and synthesized into RTL together with rest of model

## Slide 7: Catapult supports two SystemC Coding Styles
“RTL in SystemC” coding style
“Matchlib SystemC” coding style
Each has advantages/disadvantages
The two coding styles can be mixed in same design, even in same block or process

## Slide 8: “RTL in SystemC”: example 01: SC Combinational Process
HLS Input
HLS Output

## Slide 9: “RTL in SystemC”: example 02: SC Sequential Process
HLS Input
HLS Output

## Slide 10: “RTL in SystemC”: example 04: SC signal level protocols
Question: What’s the throughput?

## Slide 11: “RTL in SystemC” Rules
Code up to first wait() in process models the reset state.
  Every sc_out should be assigned reset value here.
Clock and reset use sc_in<bool>
All data IO uses sc_in<>, sc_out<>
Every loop has a wait() statement (unless fully unrolled)
  Catapult will add an implicit wait() statement if needed.
Some of the added value over real RTL:
  Catapult loop pipelining still works
  Any AC + SC datatypes can be used (ac_fixed, ac_float, etc).
  Any AC functions can be used (e.g. AC Math)
Module hierarchy and IO in RTL will be the same as in SystemC

## Slide 12: “RTL in SystemC” Rules (continued)
By default,
  Signal reads occur at preceding wait statement in SC source
  Signal writes take effect at next wait statement in SC source
  Catapult is free to insert scheduler states between SC wait statements
Use IO_MODE=fixed if you don’t want Catapult to add any states
Use #pragma hls_direct_input if you don’t want Catapult to insert pipeline registers for signal reads
  E.g. useful for CSRs which are held stable after block reset (better QOR)
Keep in mind that SC TB and DUT are modeling HW, not SW
  e.g. shared variable between 2 processes in TB or DUT may cause races
  Use sc_signal, Matchlib Connections, sc_fifo, tlm_fifo, etc., to avoid races.

## Slide 13: “RTL in SystemC” Advantages/Disadvantages
Advantages:
  Useful if RTL pin level protocols are “fixed”
  Useful for integrating with existing Verilog/VHDL RTL designs
  Useful for data_valid protocol (i.e. no backpressure) (see example 15*)
    common in time-domain signal processing
  May be a better fit for “RTL-centric” customers
Disadvantages:
  Low level of abstraction
  Larger models
  No fast TLM simulation mode
  Less automation for SV UVM verification
  Less automation for debug (e.g. no rand stall and transaction logging)

## Slide 14: “Matchlib Coding Style”: example 05: Pop/Push

## Slide 15: 05 Waveforms
Pre-HLS
Post-HLS
Question:
What’s the throughput?

## Slide 16: “Matchlib Coding Style”: example 06: Throughput Accurate

## Slide 17: 06 Waveforms
Pre-HLS
Post-HLS
Question:
What’s the throughput?

## Slide 18: “Matchlib SystemC” Coding Style Rules
Code up to first wait() in process models the reset state.
  Reset() methods on all ports should be called (both In and Out ports).
Clock and reset use sc_in<bool>
All data IO uses In<>, Out<>, or other Matchlib transaction ports
Only use of wait() is for:
  Reset state
  Loops with all non-blocking Push/Pop and no blocking Push/Pop
Use default Catapult scheduling modes only
Only use coding style documented in Mentor Matchlib examples

## Slide 19: “Matchlib SystemC” Coding Style Rules (continued)
Only use sc_in, sc_out, sc_signal when:
  You need to mix “RTL in SystemC” coding style with Matchlib blocks/processes (try to keep these cases isolated).
  You want to model CSRs which are held stable after block reset
    Enables efficient way to distribute CSR data to multiple blocks without synchronization overhead.
    Usually also want to use #pragma hls_direct_input for these CSR signal inputs

## Slide 20: Matchlib: When do you need to use Non-blocking IO?
Arbitration requires Peek or PopNB to all arbitrated inputs.
Time-based splitting and merging of transaction streams requires PushNB and PopNB (respectively)
There are cases where a process will need ALL non-blocking IO (all PopNB and PushNB), but it should be pretty rare.
  In this case the process should be kept as small / simple as possible, ideally communicating with other processes that follow the guidelines above.
  With all non-blocking IO, you will likely be modeling at very close to RTL level, and most likely HLS will just be translating SC RTL into Verilog RTL.

## Slide 21: Matchlib: Always prefer to use blocking IO over nonblocking IO.
Your models will be simpler and more likely to have a good process structure.
100% blocking IO is called KPN (Kahn Process Networks)
  KPN is deterministic
  easier to verify.
Non-blocking IO is sometimes needed, but introduces timing dependent behavior, and can make verification more difficult in some cases if the timing dependent behavior is externally visible.

## Slide 22: Matchlib: Methods for user-defined transactions (07*)
struct engine_t
{
static const int plugs = 4;
sc_uint<16> engine;
spark_plug_t spark_plugs[plugs];
static const unsigned int width = 16 + (spark_plug_t::width * plugs);
template <unsigned int Size> void Marshall(Marshaller<Size> &m) {
m &engine;
for (int i=0; i<plugs; i++)
m &spark_plugs[i];
}
inline friend void sc_trace(sc_trace_file *tf, const engine_t& v, const std::string& NAME ) {
sc_trace(tf,v.engine, NAME + ".engine");
for (int i=0; i<plugs; i++)
sc_trace(tf,v.spark_plugs[i], NAME + ".spark_plug" + std::to_string(i));
}
inline friend std::ostream& operator<<(ostream& os, const engine_t& rhs)
{
os << rhs.engine << " ";
for (int i=0; i<plugs; i++)
os << rhs.spark_plugs[i] << " ";
return os;
}
};
User’s struct/transaction
Declare HW bitwidth
Pack/Unpack to bits
SystemC standard tracing (see LRM)
Stream to text, used for transaction logging

## Slide 23: Matchlib “gotchas”
Always call set_sim_clk exactly once to identify your clock to Matchlib
(may get bad pre-HLS sim results if you forget currently)
All processes in both DUT and TB must use exact same clock and reset signals.
TB processes must be sensitive to reset.
All transaction IO methods must be called exactly on clock edges.
(may get bad pre-HLS sim results if you forget currently)
Multiple clocks and multiple resets are not currently supported.
Keep your code clean by using convenience macros for naming ports, signals, and module instances (uses -std=c++11)
Always use wait(), wait(int), never wait(sc_time) in both TB and DUT.
Matchlib TB and DUTs are “cycle models”.

## Slide 24: “Matchlib Coding Style” Advantages/Disadvantages
Advantages:
  “Throughput accurate” modeling in pre-HLS simulations for complex models
  Higher level of abstraction than “RTL in SystemC”
  Models are smaller
  Fast TLM simulation mode available
  Automation available for SV UVM verification flow
  Automation available for debug (rand stall injection, transaction logging)
  Growing Matchlib IP models available (AXI4, NOC, reorder buffers, etc)
  Verification flow for Matchlib enables pre-HLS model to be “stress tested”
Disadvantages:
  Learning curve may be longer than “RTL in SystemC” flow
  C++ compiler error messages can sometimes be difficult to decipher (use an IDE)
  Signal level protocols not as flexible as “RTL in SystemC”, however you can mix in “RTL in SystemC” where needed

## Slide 25: Catapult SystemC / Matchlib Collateral
General SystemC HLS and Matchlib Tutorials available here:
  $MGC_HOME/shared/examples/matchlib/toolkit
  Also see below:

## Slide 26: How do I model “X” in Matchlib?
How do I model a Fifo in Matchlib?
  10*, 11*
How do I model a sync (aka "barrier")
  12*
How do I model a dual port RAM shared between two processes?
  12*

## Slide 27: Does Mentor support everything in Matchlib?
No. Mentor supports all constructs documented in Catapult documentation.
Mentor supports all constructs used in examples included in Catapult.
Everything else in Matchlib is currently “open source” code that is not directly supported by Mentor
Over time, Mentor is likely to directly support a larger subset of Matchlib

## Slide 28: Timing Accuracy of Matchlib Models vs Catapult RTL
Currently:
  Intent is to be nearly throughput accurate for pipelined II=1 processes
    A bit of special handling needed for II != 1 (insert extra wait statements)
  Intent is NOT to be cycle accurate
  Latency and buffer storage capacity backannotation is not yet actively supported by Mentor

## Slide 29: Matchlib QOR
As of Catapult 10.6, expectation is that QOR of Matchlib designs is in general equivalent to Catapult C++ flow.

## Slide 30: General Guidelines for Coding for Good QOR in SC
Simulate and debug your pre-HLS model before you synthesize (!)
  Verify performance and functionality in your pre-HLS model
In SystemC HLS, you should always have:
  At least a rough idea of what your HW implementation will be (e.g. pipeline characteristics)
  An exact idea of what your module pin level interfaces are
Refine your architecture in your pre-HLS model
  Usually this is by far the most effective way to improve QOR
If functionality can easily be split into smaller processes, it is usually better to do so
  Control FSMs generated by Catapult will be smaller
  Smaller processes may be able to run in parallel

## Slide 31: Can I use “feature X” with Catapult SystemC Flow?
AC Datatypes – Yes
AC Math – Yes
AC DSP – Functions only, no hierarchy or instantiated AC channels
AC channel – No
“Interface synthesis” – Generally, No
“Interface synthesis for C arrays in single process” - Yes
Ccores – Yes
Blackboxes – Yes
Catapult Directives – Generally, Yes

## Slide 32: AXI4 Introduction and Matchlib AXI4 Models
Stuart Swan
HLS IP/Platform Architect
July 2020
Source: Notes are in Tahoma, regular, 8 point, italic, flush left, vertically aligned from the bottom of text box.

## Slide 33: Why should I learn about AXI4?
Very common on-chip bus interface
Representative of modern bus protocols, even representative “network on chip” bus protocols
  Enables Catapult users to build bus based HW accelerators
  Enables Catapult users to build bus fabrics in HLS
The Matchlib AXI4 models are high quality and in use in by Catapult users
AXI4 models and examples show how to mix control and dataflow while keeping good QOR

## Slide 34: AXI4 is a Message Passing Protocol
Message Passing is very common, goes by many names:
  Kahn Process Networks (KPN)
  “Latency Insensitive”
Matchlib Connections is also a message passing framework
  So is ac_channel
Message passing is good because:
  Deterministic
  Scalable
  Latency insensitive
  Can add pipeline registers (e.g. for long paths across chips)
  Catapult is really good at pipelining message passing models

## Slide 35: AXI4 Protocol
AXI4 is a “point-to-point” protocol between a Master Port and a Slave Port
  Master initiates reads or writes
  Slave responds
Routers, Arbiters, multi-layer bus fabrics etc can be built using AXI4 Master/Slave Ports
  Matchlib contains a number of these components
The read interfaces are completely separate from the write interfaces
  Possible (and common) to have blocks that only have read interface but not write interface (or vice-versa)
All addresses in AXI4 are byte addresses

## Slide 36: AXI4 Read Channels
AR is “Address Read” Payload
  Specifies address, burst length, beat width, etc.
R is “Read” Payload
  Returns read data from Slave Port
  Each read item is called a “beat”
Protocol is:
  Master sends AR item that specifies # of beats
  Slave always returns specified # of beats
    Even if there is an error! (e.g. if address is invalid)
  Read beats are returned in order
AXI4 Read
Master Port
AXI4 Read
Slave Port
AR Item
R Item
R Item
R Item

## Slide 37: AXI4 Write Channels
AW is “Address Write” Payload
  Specifies address, burst length, beat width etc.
W is “Write” Payload
  Contains write data to send to Slave Port
  Includes write strobes (aka “byte enables”)
  Each write item is called a “beat”
B is “Write response” Payload (tells if the write succeeded)
Protocol is:
  Master sends AW item that specifies # of write beats
  Master sends exactly # of W items specified, in order
    Even if there is an error! (e.g. if address is invalid)
  Slave port returns exactly one B item per AW item.
AXI4 Write
Master Port
AXI4 Write
Slave Port
AW Item
W Item
W Item
W Item
B Item

## Slide 38: The Plot Thickens…
AXI4 allows a maximum of 256 beats per AW or AR burst
AXI4 forbids a AR or AW burst from spanning a 4K address boundary
The last beat of every W and R item in a burst must have its “last bit” set.
These restrictions keep the size of counters and adders within bus fabric components (e.g. routers, arbiters) and slaves small and fast
Also, the 4k boundary restriction simplifies routers, assuming all slaves are located on 4k boundaries within address map.
In practice, these restrictions improve area and do not reduce thruput
However, if these AXI4 aspects are visible in user’s HLS models, the HLS models become complex and error-prone.
  So, the Matchlib AXI4 components are designed to (mostly) hide these details from user’s HLS models.
  Big value-add over RTL models that use AXI4.

## Slide 39: Matchlib Automatic Burst Segmentation
The Matchlib Automatic Burst Segmenters provide:
  Automatic burst segmentation so that AXI bursts be specified as having up to 2^32 beats
  Automatic segmentation at 4k address boundaries
  Automatic setting of the “last bit” in W items
There are separate AXI4_W_SEGMENT() and AXI4_R_SEGMENT() modules
These are instantiated in blocks with AXI4 master interfaces
  The effect is that the AXI4 protocol viewed within this block is extended as noted above
Usage of these segmenters is invisible to slaves and bus fabric components
  This is because in all simulation modes, the AXI4 protocol is strictly followed on all module interfaces

## Slide 40: Encoding of AXI4 Beat Lengths
AXI4 specifies beat lengths in AR and AW payloads
  Uses an 8 bit unsigned integer
  But, we allow lengths from 1 -> 256
  So, the AXI4 encoding is:
    “0” means “1” beat
    “1” means “2” beats
    “0xff” means “256” beats
  This encoding is visible in user models (to hide it would cost QOR).
When Matchlib AXI4 Burst segmenter is used, encoding remains the same:
  “0” means “1” beat
  “0x1000” means “0x1001” beats
  Reasons: consistency, and QOR

## Slide 41: Don’t forget…
“0” encoding always means “1” beat
Every Push(aw) must correspond to exactly one b.Pop()
If you are using burst segmentation, don’t “reach around” it and try to access the native AXI4 master ports
  Exception: r items are read from native AXI4 master read port even when read segmenter is used.
Number of beats is same regardless of success or failure:
  masters must supply number of write beats they specify in aw, slaves must consume them
  masters must read number of read beats they specified in ar, slaves must produce them

## Slide 42: $MGC_HOME/shared/examples/matchlib/toolkit/include/ram.h
Default AXI4 configuration is
64 bit data width
Ram has 1 read slave port and 1 write slave
Ram stores 64k words (64 bits each)
Read and Write slaves are fully independent and each get their own thread

## Slide 43: $MGC_HOME/shared/examples/matchlib/toolkit/include/ram.h(cont)
Need to call reset() methods for signals this process drives
If address is invalid we still need to return an “r” item, but mark it with an error code
Map byte address to word address and read data
Send read item back to master, continue if more data to read, else break out of loop if done
Automatically sets “last bit” on r item when needed
start_multi_read() is a convenience method implemented in the AXI4 read slave port.
Start waiting for any length burst read (“multi”).
Result is returned in “ar”
ar.addr will be updated to next read address if we continue
AXI4 Read
Master Port
AXI4 Read
Slave Port
AR Item
R Item
R Item
R Item

## Slide 44: $MGC_HOME/shared/examples/matchlib/toolkit/include/ram.h(cont)
Call reset for signals this process drives
Start waiting for any length burst write
Result is returned in aw
B is initialized to “success”
Pop a w item
On invalid address set write response to an error
AXI4 Write
Master Port
AXI4 Write
Slave Port
AW Item
W Item
W Item
W Item
B Item
Write the data into the ram array
If more, update aw.addr and continue, else finish
Push write response

## Slide 45: Simple Example: AXI4 DMA using MatchLib
clk
rst
r_slave0
dma_done
w_slave0
w_master0
r_master0
Control Regs
clk
rst
r_slave0
w_slave0
clk
rst
w_master0
r_master0
dma_done
DMA
CPU Stimulus
RAM
= top level of design

## Slide 46: The DMA performs a memory copy using AXI4 bursts
This IO is in parallel
This IO is in parallel
The only clock/wait is for reset state
Main compute loop gets pipelined in HLS
Entire AXI4 DMA C++ is 170 lines
RTL after HLS is 6000 lines

## Slide 47: AXI4 DMA Waveforms Before HLS (SystemC simulation)
Read and write burst streams are concurrent.
R/W bus utilization is 100%
(1 read and 1 write beat per clock cycle)
Automatic AXI4 last bit generation
Automatic AXI4 burst address segmentation
Makefile sets segmentation
size to 16 rather than 256 so
easier to see in waveforms

## Slide 48: AXI4 DMA Waveforms After Catapult HLS (Verilog Sim)
RTL waveforms are almost the same as SystemC waveforms:
- Throughput is same
- Bus utilization is the same
- HLS may have added pipeline stages (under user control)
- HLS may have increased latency (under user control)

## Slide 49: $MGC_HOME/shared/examples/matchlib/toolkit/include/dma.h
DMA command sent from slave to master process
DMA address map as seen by CPU
AXI4 read and write master ports
AXI4 read and write slave ports
DMA done interrupt

## Slide 50: $MGC_HOME/shared/examples/matchlib/toolkit/include/dma.h(cont)
Reset signals that slave process drives
Get an AXI4 write where there must be only a single beat. If there is more than one beat, single_write() will automatically deal with the AXI4 protocol error requirements
Decode the CSR write and update status fields
When start register is written issue new DMA command
Every aw.Pop needs a b.Push

## Slide 51: $MGC_HOME/shared/examples/matchlib/toolkit/include/dma.h(cont)
Instantiate DMA command channel
Between slave and master processes
Instantiate W and R Segmenters
Bind W and R segmenters to native AXI4 master ports

## Slide 52: $MGC_HOME/shared/examples/matchlib/toolkit/include/dma.h(cont)
Pop a new DMA command from slave process
Copy length, and AW and AR addresses
Reset all signals this process drives
Extended AR and AW payloads work with segmenters and allow > 256 beats
Push out AW and AR addresses to RAM
Insure full thruput of R and W channels
Copy R data to W data and push out
If ex_len is currently 0 we are done
Consume write response and send interrupt to CPU

## Slide 53: Miscellaneous AXI4 Stuff
Write strobes / “aka byte enables”
  W item has one bit per byte in data payload indicating whether a particular byte is to be written.
  Allows for precise control of which bytes are written, even if data width of beats is large
  Default constructor for W item sets wstrb bits to all 1 so default behavior is to write all bytes
  Works fine with write segmenter too.
“AXI4 Narrow transfers”
  This is when the actual data width read or written is less than the bus data width
  Supported in native AXI4 master and slave interfaces
  There are complex AXI4 rules about data alignment for narrow transfers!
  Not supported in R and W segmenters

## Slide 54: Scatter Gather DMA
Stuart Swan
HLS IP/Platform Architect
June 2020
Source: Notes are in Tahoma, regular, 8 point, italic, flush left, vertically aligned from the bottom of text box.

## Slide 55: Scatter Gather DMA Introduction
DMA modules are common in SOCs to offload data movement tasks from other blocks
The Scatter Gather DMA is a simple but representative example of common SOC blocks that use bus fabrics and which are not only datapath blocks but also include control
  Also represents typical DV aspects for SOC blocks
The DMA fully uses the AXI4 features explained previously such as automatic burst segmentation
The scatter gather DMA adds features to the simple DMA block presented previously
  Same top level interfaces as simple DMA
  Same RAM block

## Slide 56: Scatter Gather DMA block diagram
clk
rst
r_slave0
dma_done
w_slave0
w_master0
r_master0
Control Regs
clk
rst
r_slave0
w_slave0
clk
rst
w_master0
r_master0
dma_done
DMA
CPU Stimulus
RAM
= top level of design

## Slide 57: Scatter Gather Slave Address Map
Note: In previous DMA (example 08*), total_len
was in beats, but now it is a byte length

## Slide 58: Scatter Operation
Source data
Target data
Aw_addr
Ar_addr
Total_len
Scatter_len
Scatter_stride
All addresses are byte addresses
All lengths are byte lengths
total_len = scatter_groups * scatter_len
Scatter_groups

## Slide 59: Gather Operation
Target data
Source data
Ar_addr
Aw_addr
Total_len
Scatter_len
Scatter_stride
All addresses are byte addresses
All lengths are byte lengths
total_len = scatter_groups * scatter_len
Scatter_groups

## Slide 60: Copy Operation
Source data
Target data
Aw_addr
Ar_addr
Total_len
All addresses are byte addresses
All lengths are byte lengths
For copy operation, scatter_len, scatter_stride, scatter_groups are ignored
Total_len

## Slide 61: SC Testbench
If true, each iteration is a copy then a copy, else it is a scatter then a gather
Target address for first operation, source address for second operation

## Slide 62: Copy_mode = true, test_iterations = 1
TB programs dma_slave for 2 operations
1st copy operation write data
2nd copy operation write data
1st copy operation read data
2nd copy operation read data
Note: SystemC Waveforms, (not RTL)
Burst segmentation
Last bit generation
Makefile sets segmentation size to 16 rather than 256 so easier to see in waveforms

## Slide 63: Same scenario, but in RTL

## Slide 64: Copy_mode = false, test_iterations = 1
Write addresses are scattered
Note: SystemC Waveforms, (not RTL)
Write addresses are gathered
Read addresses are gathered
Read addresses are scattered

## Slide 65: Same scenario, but in RTL

## Slide 66: Keeping things simple..
To simplify both the DUT and the TB, the DUT enforces that all addresses and lengths are aligned to bus datawidth boundaries
When TB writes to “start” CSR, checks are enforced and a AXI4 error response if returned if there any errors.
When TB writes to “start” CSR
Make sure addresses and lengths are aligned
Do additional checks if not in COPY mode
Send AXI4 error code to TB if any checks fail

## Slide 67: COPY implementation in DMA
Convert byte length to beat length (AXI4 beat length encoding)
Pop next DMA command
Push out AR and AW bursts
Copy data from R to W
We are done when length is currently 0 (AXI4 beat encoding)
Pop write response from b channel

## Slide 68: SCATTER implementation in DMA
Convert byte length to beat length (AXI4 beat length encoding)
Start the AR burst, but not the AW yet
Start the AW burst for current region in the scatter groups
We are done when length is currently 0 (AXI4 beat encoding)
Copy data from R to W
Need to do b.Pop for every Push(aw)
Increment aw.addr for next scatter group region
aw.ex_len is computed based on scatter_len, not total_len
We are done when the remaining total_len is zero

## Slide 69: Homework #1 - GATHER implementation in DMA
Steps:
  Edit testbench.cpp and change copy_mode to be false
  Edit scatter_gather.h and write the code for GATHER
    This is strictly confined to the GATHER branch of the case statement.
    If you are stuck for more than 15 minutes, ask for help.
  Compile and run your SC code and make sure the TB self-check passes
  View SC and RTL waveforms – see README file in same dir.

## Slide 70: Homework #2 – Optimize the beat rate
For copy_mode = false and test_iterations = 10, make small modifications to model and synthesis directives to optimize throughput (as reported in log output as "beat rate").
Measure in both SC sim and RTL sim.
Remember your best results and approach to report to group.

## Slide 71: Homework #3 – Compare SC and RTL sim performance #1
Edit Makefile and add –O3 to CFLAGS
Edit testbench.cpp:
  Set copy_mode = false and test_iterations = 1000
  Disable SC tracing and transaction logging as shown below
  Disable LOG messages in ram.h by modifying code in testbench.h as below
Measure simulation CPU time in SC and RTL simulation as reported in log output

## Slide 72: Homework #4 – Compare SC and RTL sim performance #2
Perform same sim performance comparison as previous slide, but use Catapult Matchlib example 20_DCT_sysc
Use the same approaches as previous slide
  Note that DCT test runs long enough that a single iteration is adequate
Try to explain any performance differences from previous test

## Slide 73: Homework #5 – Matchlib SOC Verification and Debug Tutorial
Read and follow the steps in the document:
  $MGC_HOME/shared/examples/matchlib/toolkit/doc/matchlib_soc_debug_tutorial.pdf

## Slide 74: Matchlib Homework Wrap-Up and Miscellaneous Topics
Stuart Swan
HLS IP/Platform Architect
July 2020
Source: Notes are in Tahoma, regular, 8 point, italic, flush left, vertically aligned from the bottom of text box.

## Slide 75: Homework Wrap Up and Q&A
Discuss Homework assignments 1-5
Q&A

## Slide 76: Verilog Wrapper Generation
Since Matchlib models are “protocol-accurate” and support pin level interfaces, it is easy to generate Verilog RTL wrappers for them.
This makes it easy to embed Matchlib and “RTL in SystemC” models in SV UVM testbenches
  Or even in “regular old Verilog” testbenches
Wrapped SC model has identical Verilog pins as actual RTL
  So same testbench can be used for SC model as well as RTL just by swapping the DUT model.

## Slide 77: Verilog Wrapper Generation for Scatter Gather DMA
Do the following in scatter_gather dir:
This generates two files:
  scatter_gather_dma_wrap.cpp : this wraps Matchlib ports to sc_in/sc_out and exports it to Verilog
  scatter_gather_dma_wrap.v : this is the Verilog module interface declaration. It is not actually used in the mixed language simulation, it is only for documentation.
chmod +x ../bin/wrapper*py
../bin/wrapper_gen.py --clock_name clk --clock_period 1 sim_sc top.dma1

## Slide 78: Verilog Wrapper Generation for Scatter Gather DMA

## Slide 79: Verilog Wrapper Generation for Scatter Gather DMA

## Slide 80: Simulating SC Matchlib DMA with a Verilog Testbench
A simple Verilog TB for similar DMA is shown in Catapult Matchlib example 45*:

## Slide 81: Shared Memories in SystemC Designs – Approach #1
Definition: A shared memory is an array in HLS that is preserved thru HLS that is accessed by more than one thread.
Approach #1: “Make the shared memory go away”
  Use only preserved arrays which are accessed by a single thread
  Use architectural directives in Catapult to allocate ports for those rams, etc.
  Use Matchlib components such as Scratchpad, ArbitratedScratchpad, etc., to route requests from other threads to those arrays.
  If throughput is top concern, and a few extra cycles of latency is OK, this is a very robust and flexible approach.
  Pre-HLS sim will be throughput accurate under assumption that mem rd wr access to arrays within threads are not the bottleneck

## Slide 82: Shared Memories in SystemC Designs – Approach #2
Approach #2: Use memory model from Catapult Memory Generator
  This is demonstrated in 12_ping_pong_mem
  Each thread accessing memory needs a dedicated RAM port
  There needs to be some synchronization scheme to avoid data races between threads
    12_ping_pong_mem uses Connections::SyncChannel
  Catapult memory generator SC models currently need “wait(0.3, SC_NS)” statements deleted from them so they work properly in Matchlib sims
  Catapult memory generator SC models currently do not participate in Matchlib “thruput accurate” simulation mechanism, so sim will not be thruput accurate if thread has > 1 mem accesses per clock
Memory instance
Memory read operation

## Slide 83: Shared Memories in SystemC Designs – Approach #2 (cont.)
Example 12_ping_pong_mem shows shared memory shared by threads in same module.
  In this case, you do not need to explicitly code the mem read and write ports
You can also have memory ports on modules, so that memories can be external and/or shared between multiple modules.
  In this case, you do need to explicitly code the mem read and write ports on module interfaces
Memory read port
Bind memory read port to memory instance
Memory types

## Slide 84: Shared Memories in SystemC Designs – Approach #3
Approach #3: Use ac_shared<>
  This approach is currently not supported and not recommended for SC designs.

## Slide 85: Toggle Protocol Converter – Matchlib Example 13*
Toggle Protocol Converter is a simple (and useful) example of “RTL in SystemC” mixed with Matchlib style
Toggle protocol indicates that a message has been sent when the toggle signal changes
  Reliable message delivery as long as consumer process “can keep up”
  Producer and Consumer can be running at different clock rates
Toggle output
Data output
Toggle output when we output new data
Input uses Matchlib rdy/vld protocol

## Slide 86: Toggle Protocol Converter – Matchlib Example 13*
Stimulus uses Matchlib rdy/vld protocol
Input is rdy/vld protocol
Output is toggle protocol

## Slide 87: Data Valid Protocol – Matchlib Example 15*
Data Valid protocol is similar to rdy/vld protocol, except rdy signals are removed because either:
  consumers are assumed to “always be ready” to receive messages
  if consumers are not ready and messages are dropped, it is OK.
    Note: In this case, if latency of design changes from SC model to RTL, then sim results may change due to this timing sensitivity
Assumption is that if vld=true for two consecutive clock cycles, then two messages were sent.
Data valid protocol is modeled using sc_in/sc_out (ie. “RTL in SystemC” style)
This protocol is common in time domain signal processing, where each block is clocked at a particular sampling frequency and consumes one sample per clock. The valid bit indicates if the particular sample is valid.
  When a chain of filter blocks come out of reset, the first sample at the beginning of the chain will be valid, and input samples further down the chain will not be valid until the first valid sample propagates thru the chain.
  rdy/vld protocol is not suitable for such designs.

## Slide 88: Real World Design Example – 5G Receiver
Analog
Radio
ADC
Time Domain
Receiver
FFT
Freq Domain
Receiver
Error
Correction
Automatic
Gain Control
Data Valid Protocol
IQ samples which are
Ac_complex<ac_fixed>>
AXI4 and Matchlib Push/Pop
Frames, Tones, Resource Units
AXI4 and Matchlib Push/Pop Packets
You cannot apply backpressure to the antenna!
Data Valid Protocol
CPU
Control
AXI4 and
Interrupt lines (sc_signal)
Matchlib Push/Pop work over here due to discrete
transactions and framing signals – backpressure is useful
SC clock frequency dynamically changes for certain blocks for different
bandwidth modes
Approach to architectural analysis and refinement to production HLS code is presented in “car factory” tutorial in Catapult Matchlib doc directory